## Slide 1
Micro-Grid Solution

## Slide 2
Micro-grid Solution for C&I, adaptable to different scenarios
Storage Cabinets
Grid
PV inverters
Backup Cabinet
Diesel Generator
Critical Load
internet
web/app
power line
communication (RS485/ETH)
…
…

## Slide 3
Micro-Grid Solution for C&I
Storage Cabinets
PV inverters
Backup Cabinet
DG
Load
…
…
…
…
Controller
power line
communication (RS485/ETH)
Mode 1 (grid-tide):
In gird-tied mode, the backup cabinet work as the junction cabinet, both the PV and the storage cabinets are controlled together to realize different functionalities, e.g. peak shaving, self-consumption, etc.
Grid
STS

## Slide 4
Micro-Grid Solution for C&I
Storage Cabinets
PV inverters
Backup Cabinet
DG
Load
…
…
…
…
Controller
power line
communication (RS485/ETH)
Mode 2 (off-grid):
When the PV power is lager than the load, the PV supplies the load and charges the battery simultaneously.
Grid
STS

## Slide 5
Micro-Grid Solution for C&I
Storage Cabinets
PV inverters
Backup Cabinet
DG
Load
…
…
…
…
Controller
power line
communication (RS485/ETH)
Mode 3 (off-grid):
When the PV power is less than the load and the battery has sufficient energy, the PV and the battery supplies the load together.
Grid
STS

## Slide 6
Micro-Grid Solution for C&I
Storage Cabinets
PV inverters
Backup Cabinet
DG
Load
…
…
…
…
Controller
power line
communication (RS485/ETH)
Mode 4 (off-grid):
When the PV power is very low and the battery energy is insufficient , the diesel generator needs to work. At this mode, the DG will operate in an efficient woking point to supply the power to the load and charge the battery.
Grid
STS

## Slide 7
Storage Cabinet, ESS-261KLC-SA1
Efficient & Flexible
PCS supports both on-grid and off-grid applications
Multiple cabinets can be connected in parallel to support large capacity application
Safety & Friendly
Battery uses liquid cooling and PTC heating, adaptable to various harsh environments
Intrinsic & Active & Passive ultimate safety design
Smart management
Built-in EMS, support diifferent operation modes
Visualisation management, support App and Web multi-end online monitoring

## Slide 8
Storage Cabinet, ESS-261KLC-SA1, datasheet
Model | ESS-261KLC-SA1
DC Side | 
Battery Type | LFP/314Ah
Series and Parallel Mode | 1P260S
Rated Energy | 261kWh
Nominal Voltage | 832V
DC Operating Voltage Range | 650V~949V
Depth of Discharge (DOD) | 98%
AC Side | 
Type | 3P4W
AC Voltage | 400V AC
Rated AC Power | 125kW
Maximum AC Power | 138kW
Rated Grid Frequency | 50Hz/60Hz
Power Factor | -1~1
Unbalanced Load | 0~100%
System Parameters | 
Round Trip Efficiency (RTE) | ≥88%@0.5P, ≥90%@0.25P,
Operating Ambient Temperature | -30℃~50℃ (derating above 45℃)
Storage Ambient Temperature | -30℃~60℃
Operating Relative Humidity | 0~100% (No Condensation)
Operating Altitude | ≤4000m
Ingress protection rating | IP55
Anti-Corrosion | C4-M (C5-M Optional)
Cooling Type | Liquid Cooling
Fire Detection | Smoke, Temperature,CO
Fire Suppression | Aerosol/Perfluorohexanone Spray (Optional) Whole Cabinet Level: Water Spray
Explosion Protection | Directional Smoke Extraction & Explosion Venting Panel
Installation | Ground Mounting
Communication | Modbus TCP
Dimension(W*D*H) | 1000mm*1350mm*2500mm
Weight | < 2400kg
Noise | ≤70dB(A)
Standard | IEC62619,IEC62477-1, IEC/EN 61000-6-2/4, UN38.3, UN3480, EN50549-1,

## Slide 9
Backup Cabinet, PAC-375K/625K/001M-W2
High yield
Multiple power integration All-inone
Built-in voltage and current detection, grid, generator load, BESS and PVl ports power observable
Grid and load support
Seamless Off-grid switching, noninterrupt of load power
Automatic switching between grid power and generator
Flexible and reliable
Outdoor design, bettter environmental suitability
Built-in bypass switch, better system reliabllity
PAC-375K
PAC-625K
PAC-001M

## Slide 10
Backup Cabinet, PAC-375K/625K/001M-W2, datasheet
PAC-375K
PAC-625K
PAC-001M
Model | PAC-375K-W2 | PAC-625K-W2 | PAC-1M0-W2
Grid Side |  |  | 
Rated AC Input/Output Power | 375kVA | 625kVA | 1000kVA
Rated AC Input/Output Current | 543A | 902A | 1449A
Rated AC Input/Output Voltage | 400V, 3P+N | 400V, 3P+N | 400V, 3P+N
Rated Frequency | 50/60Hz | 50/60Hz | 50/60Hz
Load Side |  |  | 
Rated AC Output Power | 375kVA | 625kVA | 1000kVA
Rated AC Output Current | 543A | 902A | 1449A
Rated AC Output Voltage | 400V, 3P+N | 400V, 3P+N | 400V, 3P+N
BESS Side |  |  | 
Max. BESS Ports | 3 | 5 | 8
Rated AC Voltage | 400V, 3P+N | 400V, 3P+N | 400V, 3P+N
Max. AC Power per Port | 138kW/kVA | 138kW/kVA | 138kW/kVA
Max. AC Current per Port | 198A | 198A | 198A
PVI Side |  |  | 
Max. PVI Ports | 3 | 5 | 8
Rated AC Voltage | 400V, 3P | 400V, 3P | 400V, 3P
Max. AC Power per Port | 138kW/kVA | 138kW/kVA | 138kW/kVA
Max. AC Current per Port | 198A | 198A | 198A
GEN Side |  |  | 
Rated AC Input Power | 375kVA | 625kVA | 1000kVA
Rated AC Input Current | 543A | 902A | 1449A
Rated AC Input Voltage | 400V, 3P+N | 400V, 3P+N | 400V, 3P+N
System Characteristics |  |  | 
Off-grid switching time | <15 ms | <15 ms | <15 ms
Operating Temperature | -35℃~60℃，＞50℃ derating | -35℃~60℃，＞50℃ derating | -35℃~60℃，＞50℃ derating
Max. Working Altitude | 2000m，＞2000m optional | 2000m，＞2000m optional | 2000m，＞2000m optional
Cooling Method | Smart controlled air cooling | Smart controlled air cooling | Smart controlled air cooling
Communication Ports | CAN,RS485,Ethernet,Dry contactors | CAN,RS485,Ethernet,Dry contactors | CAN,RS485,Ethernet,Dry contactors
Ingress Protection | IP55 | IP55 | IP55
Product Standard | IEC/EN 61439-1/-2 | IEC/EN 61439-1/-2 | IEC/EN 61439-1/-2
Mechanical Parameters |  |  | 
Dimensions (W*H*D) | 700*1800*800 mm | 1200*2100*1000 mm | 1600*2100*1000 mm
Weight | 400kg | 650kg | 800kg
Installation | Floor mount | Floor mount | Floor mount

## Slide 11
Website
www.sofarsolar.com
Email
info@sofarsolar.com
Address
11th Floor, Gaoxinqi Technology Building,
District 67, Xingdong Community, Xin'an
Street, Bao'an District, Shenzhen, China